Newsgroups: comp.sys.cbm
From: rhialto@mbfys.kun.nl (Olaf Seibert)
Subject: PET RAM memory map
Organization: University of Nijmegen, The Netherlands
Date: Wed, 14 Dec 1994 19:22:02 GMT


This could be improved upon - not all locations have labels.
I must note I've never seen a PET memory map with labels, so in that
respect this is a first. I could add the locations for the Basic 1 
ROMs in a next version. Corrections welcome. Enjoy.

;	Commodore PET RAM Memory Map
;	for Basic 2 and 4 (40 and 80 columns)
;	V1.1	13 dec 1994
;
;	Note that the labels in this list are matched up against C-64
;	memory maps. All attempts were made to secure plausibility of
;	placement.
;	Locations marked with (64#..) are found by taking the label given
;	for the C-64 and comparing ROM disassemblies. Many of these
;	locations have RS-232 specific names.


 LABEL	HEX		DECIMAL
 	ADDRESS		LOCATION	DESCRIPTION

 USRPOK	0000		0  	USR Function Jump Instr (4C)
 USRADD	0001-0002	1-2    	USR Address Low	Byte / High Byte
 CHARAC	0003		3	Search Character
 ENDCHR	0004		4	Flag: Scan for Quote at End of String
 COUNT	0005		5	Input Buffer Pointer / No. of Subscripts
 DIMFLG	0006		6	Flag: Default Array DiMension / array name
 				initial / AND, OR flag
 VAUYP	0007		7	Data Type: $FF = String, $00 = Numeric
 INTFLG	0008		8	Data Type: $80 = Integer, $00 = Floating
 GARBFL	0009		9	Flag: DATA scan/LlST quote/Garbage Coll
 SUBFLG	000A		10	Flag: Subscript Ref / User Function Call
 INPFLG	000B		11	Flag: $00 = INPUT, $40 = GET, $98 = READ
 TANSGN	000C		12	Flag TAN sign / Comparison Result
 	000D		13	3: Flag to suppress PRINT or PRINT# when -ve
	000E		14	3: File# of current I/O device (as 0010)
	000F		15	3: terminal width (unused-carried over from TTY)
	0010		16	3: width of source (unused - from TTY)
        000D-000F	13-15	4: Disk Status DS$ descriptor
 	0010		16	4: File# of current I/O device (when non-zero
				suppresses INPUT prompt etc)
 LINNUM	0011-0012	17-18	Temp: Integer Value
 TEMPPT	0013		18	Pointer Temporary String
 LASTPT	0014-0015	19-21	Last Temp String Address
 TEMPST	0016-001E  	22-30	Stack for Temporary Strings
 INDEX	001F-0022	31-34	Utility Pointer Area
 RESHO	0023-0027	35-39	Floating-Point Product of Multiply
 TXTTAB	0028-0029	40-41	Pointer: Start of BASIC	Text
 VARTAB	002A-002B	42-43	Pointer: Start of BASIC	Variables
 ARYTAB	002C-002D	44-45	Pointer: Start of BASIC Arrays
 STREND	002E-002F	46-47	Pointer End of BASIC Arrays (+1)
 FRETOP	0030-0031	48-49	Pointer: Bottom of String Storage
 FRESPC	0032-0033	50-51	Utility String Pointer
 MEMSIZ	0034-0035	52-53	Pointer: Highest Address Used by BASIC
 CURLIN	0036-0037	54-55	Current BASIC Line Number
 OLDLIN	0038-0039	56-67	Previous BASIC Line Number
 OLDTXT	003A-003B	58-59	Pointer: BASIC Statement for CONT
 DATLIN	003C-003D	60-61	Current DATA Line Number
 DATPTR	003E-003F	62-63	Pointer: Current DATA Item Address
 INPPTR	0040-0041	64-65	Vector: INPUT Routine	
 VARNAM	0042-0043	66-67	Current BASIC Variable Name
 VARPNT	0044-0045	68-69	Pointer: Current BASIC Variable Data
 FORPNT	0046-0047	70-71	Pointer: Index Variable for FOR/NEXT
 	0048-0049	72-73	Y-save; op-save; BASIC pointer save
	004A		74	Comparison symbol accumulator: bits 0,1,2
				are <, =, >.
	004B-004C	75-76	Pointer to temp storage in RAM for FN DEF,
				TAN, &c
	004D-0050	77-80	Pointer to string, length and garbage
				collect constant

 TEMPF1	0054-0058		Temporary storage for FLPT value.
 TEMPF2	0059-005D		Temporary storage for FLPT value.

 FACEXP	005E		94	Floating-Point Accumulator #1: Exponent
 FACHO	005F-0062	95-98	Floating Accum.	#1: Mantissa
 FACSGN	0063		99	Floating Accum.	#1: Sign
 SGNFLG	0064		100	Pointer: Series Evaluation Constant Pointer
 BITS	0065		101	Floating -accum. #1: Overflow Digit
 ARGEXP	0066		102	Floating-Point Accumulator #2: Exponent
 ARGHO	0067-006A	103-106	Floating Accum. #2: Mantissa
 ARGSGN	006B		107	Floating Accum. #2: Sign
 ARISGN	006C		108	Sign Comparison Result: Accum. # 1 vs #2
 FACOV	006D		109	Floating Accum. #1. Low-Order (Rounding)
 FBUFPT	006E-006F	110-111	Pointer: Cassette Buffer
 CHRGET	0070-0087	112-135	Subroutine: Get Next Byte of BASIC Text
 CHRGOT	0076		118	Entry to Get Same Byte of Text Again
 TXTPTR	0077-0078	119-120	Pointer: Current Byte of BASIC Text
 	0070			INC $77
				BNE $0076
	0076			LDA $xxxx
				CMP #$3A
				BCS $0087
				CMP #$20
				BEQ $0070
				SEC
				SBC #$30
				SEC
				SBC #$D0
	0087			RTS
 RNDX	0088-008C	136-140	Floating RND Function Seed Value
 TIME	008D-008F	141-143	Real-Time Jiffy Clock (approx) 1/60 Sec
 CINV	0090-0091	144-145	Vector: Hardware Interrupt
 CBINV	0092-0093	146-147	Vector: BRK Instr. Interrupt	
 NMINV	0094-0095	148-149	Vector: Non-Maskable Interrupt
 STATUS	0096		150	Kernal I/O Status Word: ST
 LSTX	0097		151	Current Key Pressed: 255 = No Key
 SFDX	0098		   	Flag: Print Shifted Chars.
        0099-009A               Jiffy clock correction: 623rd 1/60 sec
	                        does not increment time
 STKEY	009B		155	Flag: STOP key / RVS key
 SVXT	009C		156	Timing Constant for Tape
 VERCK	009D		157	Flag: 0 = Load, 1 = Verify (Kernel)
 NDX	009E		158	No. of Chars. in Keyboard Buffer (Queue)
 RVS	009F		159	Flag: Print Reverse Chars. -1=Yes, 0=No Used
 C3PO	00A0		160	Flag: Serial Bus-Output Char. Buffered
 INDX	00A1		161	Pointer: End of Logical	Line for INPUT
        00A2		162	Not Used
 LXSP	00A3-00A4	163-164	Cursor Y-X Pos. at Start of INPUT
 BSOUR	00A5		165	Buffered Character for IEEE Bus
 	00A6		166	Key Image
 BLNSW	00A7		167	Cursor Blink enable: 0 = Flash Cursor
 BLNCT	00A8		168	Timer: Countdown to Toggle Cursor
 GDBLN	00A9		169	Character Under Cursor
 BLNON	00AA		170	Flag: Last Cursor Blink	On/Off
?SYNO	00AB		171	Cassette Sync No. (64#0096)
?NXTBIT	00AB		171	Tape EOT Flag: EOT received from tape
 CRSW	00AC		172	Flag: INPUT or GET from	Keyboard
 	00AD		173	X save in tape handling (saves cassette #)
 LDTND	00AE		174	No. of Open Files / Index to File Table
 DFLTN	00AF		175	Default Input Device (0)
 DFLTO	00B0		176	Default Output (CMD) Device (3)
 PRTY	00B1		177	Tape Character Parity
 DPSW	00B2		178	Flag: Tape Byte-Received
 PSW=DPSW
 	00B3		179	Temporary save eg. logical address or DOS
				wedge

 	00B7		183	Temp Data Area (64#00A3)

 	00B9		185	Temp Data Area (64#00A4)

 BUFPNT	00BB		   	Pointer: Tape I/O Buffer #1
       	00BC		   	Pointer: Tape I/O Buffer #2
 INBIT	00BD		189	Cassette Temp (64#00A7)
 BITCI	00BE		190	Cassette Temp (64#00A8)
 RINONE	00BF		191	RS-232 Flag: Check for Start Bit (64#00A9)
 FNMIDX 00C0            192     Index to Cassette File name/Header ID for
                                Tape write.
 PTR1	00C0		192	Tape Pass 1 Error Log
 PTR2	00C1		193	Tape Pass 2 Error Log
 RIDATA	00C2		194	Cassette Temp (64#00AA) read flags: 0=scan,
 				1-15=count, $40=load, $80=end of tape marker
 RIPRTY	00C3		195	Cassette Short Cnt (64#00AB): counter of seconds
 				before tape write / checksum
 PNT	00C4-00C5	196-197	Pointer: Current Screen	Line Address
 PNTR	00C6		198	Cursor Column on Current Line
 SAL	00C7-00C8	199-200	Pointer: Tape Buffer/ Screen Scrolling
 EAL	00C9-00CA	201-202	Tape End Addresses/End of Program
 CMP0	00CB-00CC	203-204	Tape Timing Constants
 QTSW	00CD		205	Flag: Editor in Quote Mode, $00 = NO
 BITTS	00CE		206	Cassette Temp (64#00B4): Tape read timer flag
				=IRQ enabled for Timer 1
	00CF		207	End of tape read
	00D0		208	Read character error
 FNLEN	00D1		209	Length of Current File Name
 LA	00D2		210	Current Logical File Number
 SA     00D3            211     Current Secondary Address
 FA	00D4		212	Current Device Number
 LNMX	00D5		213	Physical Screen Line Length
	00D5            213     4.80: right side of window
 TAPE1	00D6-00D7	214-215	Pointer: Start of Tape Buffer
 TBLX	00D8		216	Current Cursor Physical Line Number
 DATAX  00D9            217     Current Character to Print
 FNADR	00DA-00DB	218-219	Pointer: Current File Name
 INSRT	00DC		220	Flag: Insert Mode, >0 = # INSTs
?ROPRTY	00DD		121	Cassette Temp
 FSBLK	00DE		222	Cassette Read / Write Block Count
 MYCH	00DF		223	Serial Word Buffer
 LDTB1	00E0-00F8	224-248	3+4.40: Screen Line Link Table / Editor Temps
 SCTOP  00E0            224     4.80: first line of window
 SCBOT  00E1            225     4.80: last line of window
 SCLF   00E2            226     4.80: first column of window
 XMAX	00E3		227	4.80: Size of Keyboard Buffer
 XMAX	03EB		1003	4.40
 RPTFLG	00E4		228	4.80: Flag: REPEAT Key Used, $80 = Repeat
                                      $40 = disable
 RPTFLG	03EE		1006	4.40
 KOUNT	00E5		651	4.80: Repeat Speed Counter
 KOUNT	03EA		1002	4.40
 DELAY	00E6	        230	4.80: Repeat Delay Counter
 DELAY	03E9		1001	4.40
 	00E7		231	4.80: Chime Time
 	03EC		1004	4.40: Chime Time
	00E8		232	4.80: Home Count
	00E9-00EA       233-234	4.80: input from screen vector (from E006)
	00EB-00EC       235-236	4.80: print to screen vector (from E009)
	00ED-00F7	237-247	4.80: not used
	00F8		248	4.80: Counter to speed TI by 6/5
	03ED		1005	4.40: Counter to speed TI by 6/5
 CAS1	00F9		249	Tape Motor Interlock #1
 CAS2	00FA		250	Tape Motor Interlock #2
 STAL	00FB-00FC	251-252	I/O Start Address
 MEMUSS	00FD-00FE	253-254	Tape Load Temps
 	00FF		255	Not used
 	0100-01FF	256-511	Micro-Processor System Stack Area
 	0100-010A	256-266	Floating to String Work Area
 BAD	0100-013E	256-318	Tape Input Error Log
 BUF	0200-0250	512-592	System INPUT Buffer
 LAT	0251-025A	593-602	KERNAL Table: Active Logical File No's.
 FAT	025B-0264	603-612	KERNAL Table: Device No. for Each File
 SAT	0265-0270	613-623	KERNAL Table: Second Address Each File
 KEYD	0270-027A	624-633	Keyboard Buffer Queue (FIFO)
 TBUFFR	027A-0329	634-825	  Tape I/O Buffer #1
 	027A			  Type of tape file:
				  1=program header for SAVE "",1,0
				  2=data block
				  3=absolute load SAVE "",1,1 (VIC-20 and later)
				  4=data file header
				  5=end of tape block: SAVE "",1,2
	027B-027C		  Start address for load
	027D-027E		  End address for load
	027F-028E		  File name
 TBUFFR	033A-03F9	826-1017  Tape I/O Buffer #2
 	033A			  4: DOS byte parameter in RECORD / char ptr
	033B			  4: DOS drive 1 number
	033C			  4: DOS drive 2 number
	033D			  4: DOS length / write flag
	033E			  4: DOS 8-bit syntax checking flag
	033F-0340		  4: DOS diskette ID
	0341			  4: Length of DOS command string
	0342-0352		  4: Buffer for filename
	0353-0380		  4: Full DOS command string buffer
	03EE-037F		  4.80: Table of 80 bits to set TABs
 DELAY	03E9		1001	4.40
 KOUNT	03EA		1002	4.40
 XMAX	03EB		1003	4.40
 	03EC		1004	4.40: Chime Time
	03ED		1005	4.40: Counter to speed TI by 6/5
 RPTFLG	03EE		1006	4.40
	03F0-03F9		  4.40: Table of 80 bits to set TABs
 	03FA-03FF	1018-1023	Unused
 TIMOUT	03FC		1020	4: Flag: Kernal Variable for IEEE Timeout
        0400-8000	1024-32767      Basic program area
	0400			0 byte at start of Basic program
	0401-0402		first link to next Basic line
	0403-0404		first line number
	0405-			tokenized basic line, terminated with 00
				followed by next link

	8000-83E7	32768-33767 40 column screen memory
	8000-87EF	32768-34767 80 column screen memory

A000-AFFF	free space for 4K EPROM
B000-BFFF	3: free space for 4K EPROM
    4         3
B000-DFFF C000-DFFF	Basic keywords and operators, and general processing
E000-EFFF E000-EFFF	Mostly screen editor functions
F000-FFFF F000-FFFF	Kernel: tape processing, IEEE-488, jump table.


-Olaf.
--
___ Olaf 'Rhialto' Seibert    rhialto@mbfys.kun.nl         What's the use of
\X/  racism if you can't even see if a person belongs to your abhorred kind?